## Slide 1: Hybrid Computing for Scientific and AI Applications
Jen Fishman
CS570 Spring 2024
Professor Adnan El-Nasan
April 22, 2024

## Slide 2: What is Hybrid Computing?
Hybrid computers utilize both analog and digital circuits for computation.
Analog circuit hardware implements a model of the problem to be solved rather than running a sequential program that manipulates bits.
Digital microprocessors enable programming of the analog hardware
Output of the analog circuit is usually digitized and may be made more precise by the digital hardware
Title page Image: Output of an analog computer running a system of differential equations
known as the Aizawa attractor displayed on an oscilloscope. Ulmann, 2018)
Source: https://www.researchgate.net/figure/Schematic-diagram-of-analog-digital-hybrid-computer-At-the-same-time-there-are-many_fig2_346513733

## Slide 3
Analog semiconductor CMOS technology commonly used for
  Audio – amplifiers, filters
  Communications – RF transmitters and receivers
  Sensors – of all types including accelerometers, gyroscopes, microphones (all found in cell phones)
  Control systems – industrial automation (now mostly digital), power management
Boolean Logic
Input Signal
Analog circuits
Output Signal
In contrast to digital data, analog data is continuous in time and not limited to discrete values.
Analog Data

## Slide 4
Why is there a resurgence in interest in alternatives to digital now?
Digital computation is energy intensive. Annual world data center energy consumption is projected to exceed 1000 terawatt-hours (tWh) by 2026 (about as much as is consumed by the country of Japan)5. One study estimates that AI will account for at least 85 to 135 (tWh) of data center energy use by 20277.
Cooling AI servers requires water. One study estimates that on average a half-liter of water is consumed for every GPT–3 session6.
Energy
Water
Scientific Computations like COVID virion particle simulations run on digital super computers can each require hundreds of kilowatt hours of energy8.
Frontier Supercomputer at Oak Ridge National Laboratory
Data center with water cooling infrastructure (blue pipes)

## Slide 5: Why is there a resurgence in interest in alternatives to digital now?
Semiconductor manufacturing technology is approaching the physical limits of transistor miniaturization. 2 nm is the width of 10 silicon atoms.24
Power requirements and heat issues are limiting clock frequency.
Sustaining Moore's law beyond the current decade will require significant technological advancement and extraordinary economic investment.24
Source: https://semiengineering.com/scaling-up-and-down/
Transistor Size over 50 Years

## Slide 6: Advantages of Digital Computing
The Von Neumann architecture solves any problem given enough time and energy.
Sequential programming is intuitive and relatively easy.
Precision of output for most applications is limited only by number of bits.
Von Neumann Architecture
Adapted from Sebastian, A., Tuma, T., Papandreou, N. et al. Temporal correlation detection using computational phase-change memory​
Digital computers have dominated computing for over 50 years. Incredible technological advances in semiconductor manufacturing and microprocessor design have been achieved to optimize the performance of digital computers.
Source: Wikipedia
Intel Sunny Cove Architecture

## Slide 7: Disadvantages of Digital Computing
Memory bottlenecks degrade performance
Amdahl's Law - computing in parallel is limited
All inputs must be converted to binary
Discrete time processing causes convergence problems
Complex mathematical problems are power intensive
Complex mathematical problems are time intensive
Adapted from Sebastian, A., Tuma, T., Papandreou, N. et al. Temporal correlation detection using computational phase-change memory

## Slide 8
How Can Hybrid Computing Help?
Analog circuits solve complex mathematical problems quickly with low power consumption
Digital circuits are used to provide programmability and may be used for increased precision
In this photo a fully analog computer (on the left) is connected to an ordinary fully digital laptop and together they form a hybrid system.
Advances in analog integrated circuit technology have now made it possible to replace a large rack of patch cable connected units with a single programmable analog or hybrid chip.
Analog Paradigm Model –1 analog computer with MacBook
Source: analogmuseum.org

## Slide 9: Advantages of Hybrid Computers
Continuous time systems – no convergence problems
Low power for both scientific and AI applications – For example, IBM's analog AI chip improves computation energy efficiency 14 fold over NVIDIA chip9
O(N) time to solution for digital computers vs O(1) time to solution for analog computers
Real world phenomena such as sound and temperature are continuous in time, so sensors generally produce analog data. Digitizing is not necessary to input data into analog computer
Power consumption of the IBM analog chip compared to others
(Ambrogio, 2023)

## Slide 10
Hybrid Computing is Not New
In the 1950s and 60s hybrid and analog computers were widely used for missile and airplane design
NASA's Mercury, Gemini, and Apollo (1969 moon landing) programs relied on analog Computers
Analog computers were abandoned due to improvements in digital computer performance, size and ease of use
Until recent decades interest in hybrid computing has been minimal
Electronic analog computer of the mid-1950s used by NASA
Source: NASA

## Slide 11: Digital vs Analog Computer Circuit Building Blocks
Logic gates are the building blocks of digital computer circuits like ALUs.
Transistors are the building blocks of logic gates and are always in either an on or off state.
Digital circuits produce discrete time signals
ALU Circuit – comprised of logic gates , implements addition and subtraction
Digital Circuits

## Slide 12
Integrator
Integrator Circuit – implements mathematical integration
Resistors, capacitors and operational amplifiers (op amps) are the building blocks of analog computer circuits.
Transistors are the building blocks of operational amplifiers and operate in their linear range.
Analog elements are used to control voltages and currents.
Addition is accomplished just with wires (currents going into the same node naturally add to each other).
Analog circuits produce continuous time signals
Credit: Rutujadeshpande Wikipedia
Operational Amplifier
Analog Computer Circuits
Resistor
Capacitor
Vin
Vout
Digital vs Analog Computer Circuit Building Blocks

## Slide 13: How an Analog Computer works
Systems of equations are physically recreated with combinations of analog electronic blocks
There are multiple blocks available for each mathematical operation
There is no sequential program that manipulates bits
An analog computer is a matrix of interconnectable circuit blocks.
These blocks are networked and programmed with initial conditions to create a circuit that models the real life system. Variables are allowed to evolve with time until the solution is obtained. Time scaling is used to reduce computation time.
(Guo, 2016)
Analog Circuit Blocks

## Slide 14
Graphics source: http://labman.phys.utk.edu/phys135core/modules/m9/harmonic_motion.html
The motion of a ball on a spring is sinusoidal and can be described by a second order differential equation.
Where x is the position of the ball
k
m
x
Simple Spring Example
This analog computer circuit models the motion of the ball on the spring. The solution function, x can be obtained from the circuit node after the second integrator from the left.

## Slide 15
Attractors are dynamical systems that are studied across a broad range of disciplines from biology to astronomy.
System of Equations
Analog Computer Solution plotted for all values of (x,z)
Dynamical System Example -Aizawa attractor

## Slide 16
Hybrid Continuous Discrete Computer (HCDC)
In 2016, Columbia University researchers designed and fabricated a 65nm CMOS hybrid computer chip prototype called the Hybrid Continuous Discrete Computer (HCDC)
The HCDC realizes a new paradigm: continuous time hybrid computation.
It is programmable and scalable.
Analog accuracy is improved with digital calibration.
The HCDC is the first and only continuous time hybrid computer in existence today.
Die photo of HCDC Device
Source: N. Guo et al., "Energy-Efficient Hybrid Analog/Digital Approximate Computation in Continuous Time," in IEEE Journal of Solid-State Circuits

## Slide 17
SPI controller is programmed through external board.
Computation results can be digitized on chip and output through SPI.
Ning Gui et al, Energy-Efficient Hybrid Analog/Digital Approximate Compuation in Continuous Time, IEEE Journal of Solid Srate Ciricuits
Block diagram of a hybrid analog 65 nm CMOS prototype chip, produced by Columbia University researchers led by Ning Guo
HCDC Architecture
Digital
Analog
Analog and digital ADC, SRAM and DAC circuits on this chip operate in continuous time, preventing convergence and aliasing (sampling) problems.
ADC, SRAM, and DAC are event driven. There is no clock, so no clock period latency or power wasted on clock distribution.

## Slide 18
Hybrid Computing Unit Workflow
Hybrid Computing Unit Architecture Layers
HCDC Workflow and Architecture Layers
Guo, 2016
Guo, 2016

## Slide 19: HCDC Implementing a Differential Equation
(Guo, 2016)
x1: position of Mass A
x2: position of Mass B
k1, k2, k3 : spring constants
Types of analog blocks:
Real world system:
System of differential equations and circuit realization of the system:
(Guo, 2016)
(Guo, 2016)

## Slide 20: Performance Comparison HCDC vs Sleep Walker, an MSP430 Based Ultralow power Microcontroller
 | Coupled mass-springs 4.7% RMS error |  | Van der Pol 4.6% RMS error | 
 | Analog chip | MSP430 Digital Chip | Analog chip | MSP430 Digital Chip
Time step size (s) | N/A | 0.85 | N/A | 0.23
No. of iterations | N/A | 47 | N/A | 260
Clock cycles per iteration (est.) | N/A | 21.6k | N/A | 7.15k
Total Clock cycles | N/A | 1015k | N/A | 1859k
Solution time (us) | 320 | 41k | 480 | 74k
Solution energy (uj) | 0.25 | 7 | 0.14 | 13
MSP430 is a low power, 16 bit RISC CPU microcontroller optimized for portable measurement applications.

## Slide 21: Analog Circuit Limitations
The computer may not have enough computational elements to model the problem.
Analog circuits do not have the precision of digital circuits.
Precision analog chips are more difficult and costly to manufacture than digital chips.
Source: Flickr , creator: x-ray delta one

## Slide 22: Hybrid Scientific Computing Summary
Hybrid computers:
Find solutions by simulating a system of equations using analog circuits
Process data in its analog form - do not convert data to binary
Are programmed by configuring circuit block connections, input signals and initial conditions
Allow variables to evolve with time until the solution is obtained
Energy consumption has been shown to be an order of magnitude less than comparable digital circuits
Computation has been shown to be more than two orders of magnitude faster
Source: analyticsteps.com

## Slide 23: Analog Neuromorphic Computing
Neuromorphic analog computation is the subject of much research by many universities and corporations. From behemoth corporations such as IBM and Intel to small start ups like Mythic AI, neuromorphic analog chip development efforts are underway and gaining much attention. Novel circuit elements such as phase-change memory devices and memristors hold potential to revolutionize AI.
Mythic (2024)

## Slide 24: Analog Neuromorphic Computing
A Deep learning neural network (DNN) like GPT-4 has trillions of weighted connections (parameters).
Weights must be programmed during training and accessed and multiplied during inference.
The workload for digital circuits, even for GPUs (or TPUs ), for the task, is power intensive.

## Slide 25
How could Analog Circuits help?
Von Neumann architecture is not a good fit for massively parallel neural networks (Amdahl's law) but analog computation is inherently completely parallel.
Prototype analog neural network implementations consume a fraction of the energy of their digital counterparts with the same compute performance.9,10
Neural networks do not require high precision.

## Slide 26
Multiply Accumulate
Multiply accumulate computes the product of two numbers and adds that product to an accumulator.
It is implemented digitally as a fused operation - the entire calculation is done in full precision and the result is rounded. The block diagram to the left doesn't appear very complicated, but typical implementations are more like the diagram to the right.
General Architecture of a MAC
Source: Seo, Young-Ho A New VLSI Architecture of Parallel Multiplier–Accumulator Based on Radix-2Modified Booth Algorithm
Neural networks use multiply accumulate operations to determine if incoming signals to an individual neuron will result in that neuron "firing" and propagating the signal to its output connections.

## Slide 27: Problems with GPUs
When GPUs are used to operate a DNN, billions of multiply-accumulate(MAC) operations are required to process even a low resolution image stream
Energy usage is high – during training as well as inference - a problem for servers as well as low power IOT edge devices
Space requirements are high
Temperature regulation is difficult
Processing must occur in the cloud – another problem for IOT edge devices
GPT-4 required 25 x 1025 FLOPs to train. Estimates vary widely of GPU energy consumption for this process but using a generous 10009 FLOPS/Watt12 GPT-4 GPUs used up 69.4 MWh. This amount could power 77 U.S. homes for one month.14
Estimated total floating point operations (FLOPs) required to train Machine Learning Systems from 1950 to 2023
Source: Centre for the Governance of AI, Original Data from Epoch.

## Slide 28: More Problems with GPUs – Memory Accessing
Neural networks need to access weight data
Each weight may be needed only once so weights are not cached
Reducing memory accesses by pruning paths (reducing the number of parameters) not considered important to the functioning of the network significantly complicates development
Source: NVIDIA

## Slide 29: Analog Multiply Accumulate in Memory
Tunable resistors serve as memory elements – these are the weights of the neural network that are varied during training
Neural network input vectors are voltages and outputs are currents
Matrix multiplication happens in memory - "compute in memory"
Hundreds of thousands of MAC operations occur in parallel
A straight-forward solution to implement matrix multiplication is to use a simple analog component, a resistor, as a weight storage element and apply network inputs as voltages across the resistor.
Mythic (2024)
Burr (2021)

## Slide 30: Memristors
Nanoscale devices that retain state without power
Act as electronic synapses
Resistance can be varied continuously to represent analog syapse weights
Resistance depends on the magnitude and direction of current that had previously flowed through the device
Fabrication has been shown to be compatible with CMOS process
Research is ongoing on many different implementations, many using metal oxides
Memristor Symbol
(Adapted from Cao, 2023)

## Slide 31: Protonic Programmable resistors
Nanometer scale resistors compatible with silicon semiconductor fabrication process
Proton insertion changes conductivity of phosphosilicate glass resistor to modify weights
10,000 times faster than human synapse – 5 nanosecond operation.
Highly energy efficient
Capable of operation over millions of programming cycles
False-colored top-view scanning electron microscope image of a fabricated protonic resistor with a 30-nm–by–60-nm channel.

## Slide 32: Phase Change Memory (PCM)
Constructed by placing a material that changes state when voltage is applied to it between to electrodes
State of material changes from solid to amorphous when voltage pulse is applied.
Nanoscale devices usually made of a combination of Germanium, Antimony and Tellurium.
Can be engineered to optimize desired characteristics such as non-volatility and programming speed.
Much research on novel materials for PCM is on going
Manuel Le Gallo, IBM Research - Europe
PCM Programming Process

## Slide 33
Mythic M1076 Analog Matrix Processor
(Mythic, 2022)
(Mythic, 2022)
(Mythic, 2022)
Flash transistors used as tunable resistors
Mythic workflow generates and installs network chip configuration from network graph.
Connects to host via PCIe

## Slide 34: Mythic M1076 Analog Matrix Processor Architecture
Tile based system
76 Analog Compute Engine Tiles
5 Sector Control Tiles
1 PCIe tile
1 System control tile
Capacity for 80 Million DNN weight parameters
Regardless of type, each tile contains:
64kB SRAM
32 bit RISC-V core
Single Instruction Multiple Data (SIMD) vector engine
Network-on-chip router

## Slide 35: Analog Compute Engine Tile
The RISC core controls matrix multiply operations performed by the Analog Compute Engine (ACE)
Flash transistors are used as tunable resistors to store weights inside the ACE.
ADCs convert result to digital.
Calculation result is moved to output buffer to be output to local SRAM or another tile. Activation function is applied at this stage.
(Mythic, 2022)
Mythic ACE Flash Resistor Matrix

## Slide 36
Estimated Energy for training calculation:
FLOPs = Floating point operations
FLOPS = Floating point operations per second
Mythic FLOPS per Watt = 7.14 x 1013 FLOPS/Watt (reference 13)
NVIDIA FLOPS per Watt = 1012 FLOPS/Watt this is the theoretical limit based on NVIDIA A100 manufacturer's specifications in actuality it may be significantly lower (reference 12)
Mythic estimates that its chip reduces power by a factor of 10 over digital processors.(reference 13)
Mythic chips cannot be used for training, the comparison is to demonstrate power savings at this scale of use.
Energy Usage Comparison
Training GPT-4 Total FLOPs (Estimated)11 | 25 x 1025 | 
 | NVIDIA A100 | MYTHIC 1076
FLOPS/Watt | 1012 | 7.14x1013
Energy | 69.4 MWh | 9.7 MWh
Energy = Total FLOPs
FLOPS/Watt
The difference in energy of 59.7 MWh is roughly equivalent to the average monthly energy used by 60 U.S. households.14

## Slide 37: Summary and Conclusion
Hybrid computing takes advantage of the low power requirements and high speed performance of analog computers and the flexibility and precision of digital ones.
Hybrid computing has potential to solve complex mathematical systems for scientific researchers while conserving energy resources.
Hybrid computing is especially well suited for low power IoT edge devices.
Hybrid neural networks have potential to ease the increasing power demands of deep neural network training and inference
Analog memristors are being investigated by many teams to develop fast, low power variable resistance elements ideal for use in deep neural networks.
Other devices like phase change memory and photonic resistors also hold promise as memory elements for AI.

## Slide 38: Remarks
I enjoyed learning about analog computation and how phenomena in the real world, which are described by differential equations, can be modeled using electronic components. For me this is an exciting reemergence of an old computing paradigm from before the proliferation of the digital computers and I hope the research and development of hybrid computers continues and has significant impacts.
I did struggle to keep the project relevant to the class, as many of the papers I read discussed analog circuit design in great detail and so were in large part beyond the scope of my project. This topic calls attention to the weaknesses of the Von Neumann architecture in the context of AI and scientific computing and in doing so I hope it creates a greater depth of understanding in all of these areas and provokes thought and creativity towards solutions, whether they involve hybrid computing or not.
While researching this project, I refreshed my basic knowledge of differential equations and learned more deeply about dynamical systems, both of which were unexpected but highly interesting. I gained an in depth understanding of the HCDC chip architecture and some of the design choices they made, although much of this was not relevant to this class. There is a lot of exciting research underway relating to hybrid computing at present, involving both new systems and materials. I hope that this project helped familiarize the class with some of the innovative research that may transform computation in the future.
I am interested in doing more research in the field of analog computing and the development of analog chips for scientific computing applications. I also have a long standing interest in neuromorphic circuits and deep neural networks and would like to continue to make them part of my studies.

## Slide 39: References
Tsividis, Y. (2017, December). Not your Father's Analog Computer, IEEE Spectrum. https://spectrum.ieee.org/not-your-fathers-analog-computer
Sebastian, A., Tuma, T., Papandreou, N. et al. (2017) Temporal correlation detection using computational phase-change memory. Nat Commun 8, 1115. https://doi.org/10.1038/s41467-017-01481-9
Summary of Dynamic System Simulation Technology Based on Computer Simulation Model - Scientific Figure on ResearchGate. Available from: https://www.researchgate.net/figure/Schematic-diagram-of-analog-digital-hybrid-computer-At-the-same-time-there-are-many_fig2_346513733 [accessed 18 Apr, 2024]
Buckley, S. (2024, March). IEA Study Sees AI, Cryptocurrency Doubling Data Center Energy Consumption by 2026. Data Center Frontier. https://www.datacenterfrontier.com/energy/article/33038469/iea-study-sees-ai-cryptocurrency-doubling-data-center-energy-consumption-by-2026
International Energy Agency. Electricity Consumption. https://www.iea.org/reports/electricity-information-overview/electricity-consumption
Berreby, D. (2024, February) As Use of A.I. Soars, So Does the Energy and Water It Requires, Yale Environment 360. https://e360.yale.edu/features/artificial-intelligence-climate-energy-emissions
Sparks, M. (2023, Oct) Should we be worried about AIs growing energy use? NewScientist. https://www.newscientist.com/article/2396064-should-we-be-worried-about-ais-growing-energy-use/?_ptid=%7Bkpdx%7DAAAAwt3ylrzzhAoKcmJhNGYxWmNwZRIQbHY2eGJ6OGxxYnA4dm1oNRoMRVg1Q1FOVDBDT0tYIiUxODIzb2ZvMGRrLTAwMDAzM25uYWg3NXB2dDY4dTdlamliczQ0KhtzaG93VGVtcGxhdGVWOVNaN1BOS1FBVFQ0NzQwAToMT1RDTzJDNlc2NEhGQg1PVFYwVjRDS1A5QTBWUhJ2LYUA8Bl2c2prdXVuaXJaDjcxLjExNy4xNDQuMTk1YgNkd2No8eyPsQZwE3gE
Shankar, S. (2023, October). Energy Estimates Across Layers of Computing: From Devices to Large-Scale Applications in Machine Learning for Natural Language Processing, Scientific Computing, and Cryptocurrency Mining, Computers and Society. https://arxiv.org/abs/2310.07516
Ambrogio, S., Narayanan, P., Okazaki, A. et al. (2023, August) An analog-AI chip for energy-efficient speech recognition and transcription. Nature 620, 768–775 https://doi.org/10.1038/s41586-023-06337-5

## Slide 40: References
10. Huang, Y., Guo, N., Seok, M.,Tsividis,Y. and Sethumadhavan,S. (2016) Evaluation of an Analog Accelerator for Linear Algebra. ACM/IEEE 43rd Annual International Symposium on Computer Architecture (ISCA), Seoul, Korea (South),pp. 570-582, doi: 10.1109/ISCA.2016.56. https://ieeexplore.ieee.org/document/7551423
11. Epoch Database, https://epochai.org/data/epochdb/table and colab notebook linked to table https://colab.research.google.com/drive/1O99z9b1I5O66bT78r9ScslE_nOj5irN9?usp=sharing
12. Desislavov, R., Martínez-Plumed, F., & Hernández-Orallo, J. (2021). Compute and energy consumption trends in deep learning inference. arXiv preprint arXiv:2109.05472. https://arxiv.org/abs/2109.05472
13. Mythic. (2022). Mythic Highlights its Power-Efficient AI Solution and Previews Next-Gen Architecture. https://mythic.ai/whats-new/mythic-highlights-the-companys-power-efficient-ai-solution-and-previews-next-gen-architecture/#:~:text=This%20was%20highlighted%20with%20a,to%20a%20whole%20new%20level.
14. U.S. Energy Information Administration. Frequently Asked Questions. https://www.eia.gov/tools/faqs/faq.php?id=97&t=3
15. Burr, G., Sebastian, A., Ando, T., Haensch, W. (2021, November). The Femtojoule Promise of Analog AI. IEEE Spectrum. https://spectrum.ieee.org/analog-ai
16. Guo, N. et al. (2016, July). Energy-Efficient Hybrid Analog/Digital Approximate Computation in Continuous Time. IEEE Journal of Solid-State Circuits. Vol. 51, no. 7, pp. 1514-1524. https://ieeexplore.ieee.org/document/7463004
17. Guo, N., et al. (2015, September). Continuous-time hybrid computation with programmable nonlinearities. ESSCIRC Conference 2015 - 41st European Solid-State Circuits Conference (ESSCIRC). Graz, Austria, pp. 279-282. https://ieeexplore.ieee.org/document/7313881
18. Mythic. (2022). Taking powerful, efficient inference to the edge[White paper]. https://mythic.ai/wp-content/uploads/2022/02/MythicWhitepaper-2019oct31.pdf
19. Ulmann, B. (2018, December) The Aizawa attractor. Analog Paradigm Application Note #17. https://analogparadigm.com/downloads/alpaca_17.pd
20. Onen, M, et al. (2022, July). Nanosecond protonic programmable resistors for analog deep learning. Science. Vol 377, Issue 6605, pp. 539-543. https://www.science.org/doi/10.1126/science.abp8064#body-ref-R14
21. Cao, Z., Sun, B., Zhou, G., et al. (2023 March). Memristor-based neural networks: a bridge from device to artificial intelligence. Nanoscale Horizons. Vol 8, pp. 76-745. https://pubs.rsc.org/en/content/articlelanding/2023/nh/d2nh00536k
22. [Onur Mutlu Lectures]. (2023, November 6). Deep Learning Inference Using Computational Phase-Change Memory [Video]. You Tube. https://www.youtube.com/watch?v=cEAirlU_KeY
23. Schenk,F. M., Zellweger, T., Dhananjeya, K., et al. (2024). Phase-Change Memory from Molecular Tellurides ACS Nano. 18 (1), pp. 1063-1072. https://pubs.acs.org/doi/10.1021/acsnano.3c10312

## Slide 41: References
24. Mckenzie, J. (2023, June). Moore's law:further progress will push hard on the boundaries of physics and economics. Physicsworld. https://physicsworld.com/a/moores-law-further-progress-will-push-hard-on-the-boundaries-of-physics-and-economics/